## Slide 1
Dynamic Spatially Isolated Secure Zones for NoC-based Many-core Accelerators
Maria Méndez Real, Vincent Migliore, Vianney Lapotre, Guy Gogniat
Lab-STICC Université de Bretagne-Sud Lorient FRANCE
Philipp Wehner, Diana Göhringer
Ruhr-University Bochum, GERMANY

## Slide 2
Context: NoC-based many-core accelerator
A controller is in charge of the deployment of the applications on the accelerator
Trusted and untrusted processes executing in parallel sharing resources
-> cache-based Side-Channel Attacks (SCA)
V: Victim
A: Attacker

## Slide 3
Cache-based Side-Channel Attacks due to cache sharing
Principle:
  Caches are seen as leakage channels
  The attacker behaves as a normal process
  Analyzes its own activity
  Determine cache lines or sets accessed by the victim
  Deduce sensitive information
Various implementations
  AES, RSA, ECC
  Different architectures (Intel, AMD, ARM) [2]
Context: Cache-based Side-Channel Attacks
[2] “Y. Yarom, et al., “FLUSH+RELOAD: A High Resolution, Low Noise, L3 Cache Side-Channel Attack”, in the 23th USENIX Security Simposium, 2014.

## Slide 4
Countermeasures against access-driven attacks
[3] J. Blomer and V. Krummel, “Analysis of Countermeasures Against Access Driven Cache Attacks on AES,” Selected Areas in Cryptography,vol. 4876, pp. 96–109, 2007.
[4] Guanciale, et al., “Cache Storage Channels: Alias-Driven Attacks and Verified Countermeasures,” in IEEE Symposium on Security and Privacy, 2016.
[5] Wang and R. B. Lee, “New Cache Designs for Thwarting Software Cache-based Side Channel Attacks,” in IEEE Symposium on Computer Architecture (ISCA), 2007, pp. 494–505.
[6] www.arm.com/products/processors/technologies/trustzone/
Software countermeasures:
  Changing the implementation of cryptographic algorithms [3]
Hardware countermeasures:
  Disabling cacheability
  Flushing the cache after each context switch [4]
  Changing the cache design -> Partitioned cache [5]
  Two separate virtual worlds on the same processor [6]
Application specific
Too expensive
-> not doable
Solution at the processor level only

## Slide 5
Spatial isolation for sensitive applications
The NoC is secured
How can this be achieved?
Expected under utilization of resources, how can the performance overhead be evaluated?

## Slide 6
Implementation
A dedicated processor behaves as a controller of the platform
Evaluation of different deployment strategies for the controller
  Scheduling
  Monitoring of the platform state
  Resource allocation algorithms
  Secure zones creation strategies
SW controller is trusted
[7] M.Méndez Real et al., “ALMOS many-core operating system extension with new secure-enable mechanisms for dynamic creation of secure zones,” in Proc. of Euromicro international Conference on Parallel, Distributed and Network-Based Processing (PDP), 2016.

## Slide 7
Secure-enable mechanisms
Scheduling: Round Robin
Monitoring: Quaternary decision tree structure
Task mapping: Leverage the data accesses locality
M : Memory utilization rate
U : Processor utilization
S : Secure zone dedicated
M
M
M
M
M
U
U
U
U
U
S
S
S
S
S
c0
c2
total
C
0
c1
c3
C
2
C
1
C
0
c0
c1
c2
c3
C
1
C
2
C
0

## Slide 8
Secure-enable mechanisms
Isolated application -> secure zone creation:
  Static SZ size
M : Memory utilization rate
U : Processor utilization
S : Secure zone dedicated
M
M
M
M
M
U
U
U
U
U
S
S
S
S
S
c0
c2
total
C
0
c1
c3
C
2
C
1
C
0
c0
c1
c2
c3
C
1
C
2
C
0
Active cluster
Secure zone cluster
Idle cluster

## Slide 9
Secure-enable mechanisms
Isolated application -> secure zone creation:
  Static SZ size
  Dynamic SZ size
M : Memory utilization rate
U : Processor utilization
S : Secure zone dedicated
M
M
M
M
M
U
U
U
U
U
S
S
S
S
S
c0
c2
total
C
0
c1
c3
C
2
C
1
C
0
c0
c1
c2
c3
C
1
C
2
C
0
Active cluster
Secure zone cluster
Idle cluster

## Slide 10
Virtual prototyping: OVP-based MPSoCSim [8]
Experimental protocol:
4x4 clusters architecture (60 MB + 1 ARM)
Matrix multiplications, 17 parallel tasks for each multiplication
5 applications -> 85 tasks running in parallel
Experimental setup
Different deployment strategies:
Secure zones of fixed size
Secure zones with dynamic size
Different execution scenarios:
Baseline scenario
One isolated application arriving at first
One isolated application at the middle of the execution
Three isolated applications
Maximum parallelism (5 clusters)
Limited resources (4 clusters)
[8] M.Méndez Real et al., “MPSoCSim extension: An OVP Simulator for the Evaluation of Cluster-based Multicore and Many-core architectures,” in Proc. Workshop on Virtual Prototyping of Parallel and Embedded Systems (ViPES) as part of the International Conference on Embedded Computer Systems: Architectures, Modeling, and Simulation (SAMOS XV), 2016.

## Slide 11
Results
Total execution time normalized to the baseline scenario:
b. One isolated application with the highest priority
c. One isolated application with a medium priority
d. Three isolated applications
Up to 30% overhead
Negligible overhead when no load

## Slide 12
Exec. time of non isolated, isolated application (in msec.) and in average:
1. Static SZ
size
(5 clusters)
2. Static SZ size
(4 clusters)
3. Dynamic
SZ size
b. One isolated application with the highest priority
c. One isolated application with a medium priority
d. Three isolated applications
The dynamic strategy leverages the performance of non isolated applications
Results
The static (5 clusters) strategy leverages the performance of isolated applications

## Slide 13
1. Static SZ size
(5 clusters)
2. Static SZ size
(4 clusters)
3. Dynamic SZ size
Resources utilization rate:
The dynamic strategy achieves the highest resource utilization rate
Results

## Slide 14
Spatial isolation of sensitive applications VS cache-based SCA
Evaluation on different execution scenarios with different strategies through virtual prototyping
According to the deployment strategy, isolated or/and non isolated applications performance is leveraged
Future work: NoC protection
Conclusion and future work

## Slide 15
Thank you for your attention!